## Slide 1: Automotive Media Center with Real-time GPS tracking.
Presented by:
Clint Bhola

## Slide 2: Overview
Every year about 700,000 vehicles get stolen in US. In fact, a car is stolen every 45 seconds.
Implement a simple cost effect way to track your vehicle if its stolen.
The advent of powerful embedded systems allows us to create many Sci-Fi fantasies.

## Slide 3: Deliverables
Building a cheap but effective Global Car Tracking and remote control System.
Creating high-tech a multimedia car system that also provides turn by turn Navigation.
Exporting data to the cloud for in-dept driving logs as well as real time tracking.

## Slide 4: Global Car Tracking and Remote Control System
Hardware
  Arduino Uno – microcontroller board based on the ATmega328
  Arduino GSM Shield (SM5100B-D) - miniature, quad-band GSM 850/EGSM 900/DCS 1800/PCS 1900 module
  GPS Module (Adafruit Ultimate GPS) - 66 channel w/10 Hz updates [MTK3339 chipset]
Software
  Arduino IDE
    Software Serial Library
    Tiny GPS Library

## Slide 5: Global Car Tracking and Remote Control System
Technology
  The ‘Software Serial Library’ creates additional Rx and Tx interfaces on unused digital pins.
  Uses a serial monitor software to issue commands and read output from the Serial ports.
  TinyGPS Library; provided by Adafruit provides methods for aquiring lat, lon and speed from GPS module.

## Slide 6: Global Car Tracking and Remote Control System
Remote Control
  Text messages can be used to control key features of the car (engine, headlights, horn, etc)
  Once GSM module receives the correct information e.g. #Engine1, it turns on a preprogrammed digital IO pin which in will in turn start the car.

## Slide 7: Global Car Tracking and Remote Control System
Text for location
  Text a specific password (‘findme’) to the GSM module to receive cars current location via sms.
  Text will contain lat, lon information which can then be used to find cars location through Google maps.

## Slide 8: Global Car Tracking and Remote Control System
Syncing to the AWS Cloud
  Amazon EC2 Ubuntu Server instance
    Plone and Zope
      creation of webpage with embedded Google Maps API.
      Relational Database adapter using MySQLdb and ZMySQLDA
    MySQL
      Creates the table where information from the tracking module will be stored.
    Python Twisted
      Create a simple console server
      Outputs data to terminal

## Slide 9: Multimedia System
Hardware
  Raspberry Pi B+
  7” touch screen module
  -USB GPS Module
Software
  Raspbain
  Navit
  XBMC

## Slide 10: Multimedia System
Operating System
Raspbian
  Rebuilt and recompiled Raspbain Kernel to include touch screen support and calibration software.
  Firmware also had to be modified to allow for touch screen abilities.

## Slide 11: Multimedia System
Turn by Turn Navigation
Navit
  Open source navigation software.
  Free maps available for a wide range of locations worldwide.
  Provides voice guided navigation.
  Touch screen support

## Slide 12
Full Media Center
XBMC
  Media-Center Software
  Supports all audio and video formats
  Touch screen support

## Slide 13: Project Future
Cloud Database
  Tidy up coding and make a stream line webpage that would allow for tracking logging and sharing of data.
Media Center
  Use more GPIO pins for control of in car functions, through GUI.